Suggested Specifications For Onyx Valve

Pinch Valves

Series CEP Electrically Operated Pinch Valves

Valves shall be full cast metal body, mechanical pinch type with flange ends on both body and sleeve.  Closing shall be accomplished by a single pinching mechanism.  The valve stem shall be rising, non-rotating, stainless steel, with ACME class 2G threads, driven by a bronze alloy drive nut.  The sleeve shall be one-piece construction with integral flanges drilled to ANSI B16.1 Class 125 standard.  Flanges shall have through holes, and shall be designed to accommodate a standard hex nut per ANSI B18.2.2; tapped flanges are not acceptable. To prevent binding in the event of a sleeve failure, the stem threads shall always remain outside the valve bonnet assembly, and shall be completely isolated from the process fluid, even if the sleeve fails.

The rubber sleeve shall be provided with molded-in Positive Opening Tabs to insure full opening after the valve has been closed for extended periods of time.  Rubber sleeve shall be reinforced with polyester fabric or nylon cords.

Valves shall be Onyx series CEP or approved equal.